## Slide 1: CS230: Digital Logic Design and Computer Architecture
Lecture 22: DRAM Organization and Controller
https://www.cse.iitb.ac.in/~biswa/courses/CS230/autumn23/main.html

## Slide 2: DRAM Organization
Channel
Rank
Chip
Bank
Row
Column
Rank 0 with 8 chips
Rank 1 with 8 chips
DIMM

## Slide 3: Rank
DIMM (Dual in-line memory module)
Side view
Front of DIMM
Back of DIMM
Rank 0: collection of 8 chips
Rank 1

## Slide 4: Ranks, Banks, Rows, Columns
Rank 0
Rank 1
DIMM
Bank 0
Bank 1
Bank 2
Bank 3
Multiple Chips

## Slide 5: Ranks, Banks, Rows, Columns
Rank 0
64 bits
16
16
16
16
Bank
Row
Column
Chip
Bank 0
Bank 1
Bank 2
Bank 3
X16 device (DRAM width, # output pins)
16-bit interface: 16 bits from each chip in one go

## Slide 6: Ranks, Banks, Rows, Columns
Each rank has 64-bit wide data bus
If a rank is of width x8 then # DRAM chips ??
What about x4, # DRAM chips ??
If a rank is of width x8 then # DRAM chips ?? 8
What about x4, # DRAM chips ?? 16

## Slide 7: Row Decoder and Row buffer (Sense Amplifier)
Column mux
Row Decoder
Row Buffer
Each bank has a row buffer
Stores the last used row
2KB

## Slide 8: An Example
2Gb * 8 DRAM Chips (one side of the rank)
Total 16 chips + 2 chips for ECC (for both the ranks)
64 bit + 8 bit ECC interface (72 bit wide DIMM)
Transferring a 64B cache line will take 8 transfers of 8B each
8B will come from 8 chips (8 bits from one chip)
1 bit from each DRAM array assuming 8 DRAM arrays per bank

## Slide 9: DRAM to LLC interaction
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
. . .

## Slide 10: DRAM to LLC interaction
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
Row 0
Col 0
. . .

## Slide 11: DRAM to LLC interaction
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
8B
Row 0
Col 0
. . .
8B

## Slide 12: DRAM to LLC
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
8B
8B
Row 0
Col 1
. . .
8 cycles (DRAM IO): 1 cycle transfers 8 bytes from a column

## Slide 13: DRAM Address Mapping (One Channel)
Low Col.
High Column
Row (14 bits)
Byte in bus (3 bits)
Bank (3 bits)
3 bits
8 bits
Column (11 bits)
Bank (3 bits)
Row (14 bits)
Byte in bus (3 bits)
2GB DRAM, 8 Banks, 16K rows, 2K Columns per bank
Row Interleaving: Consecutive rows in consecutive banks
Cache Interleaving: Consecutive cache blocks in consecutive banks

## Slide 14: Row Access
A “DRAM row” is also called a “DRAM page”
“Sense amplifiers” also called “row buffer”
Each address is a <row,column> pair
Access to a “closed row”
  Activate command opens row (placed into row buffer)
  Read/write command reads/writes column in the row buffer
  Precharge command closes the row and prepares the bank for next access
Access to an “open row”
  No need for activate command

## Slide 15: Row Buffer hit/miss/conflict
Row Buffer
(Row 0, Column 0)
Row decoder
Column mux
Row address 0
Column address 0
Data
Row 0
Empty
(Row 0, Column 1)
Column address 1
(Row 0, Column 85)
Column address 85
(Row 1, Column 0)
HIT
HIT
Row address 1
Row 1
Column address 0
CONFLICT !
Columns
Rows
Access Address:

## Slide 16: DRAM Timing Constraints
tRAS: Row address strobe latency
tRP: Precharge latency
tCAS: Column address strobe latency
tRC: Row cycle time: tRAS+tRP

## Slide 17: Row (Page) Policies
Open Page (do not get confused with an OS page)
After an access: Keep the page in the row-buffer
Consecutive accesses to the same page : Row-buffer Hit
On an access to different page: Close the row and open the new one
Closed page:
After an access: Close the page if there are no accesses to the same row in the request queue.
Consecutive accesses to different page : Low latency
On an access to different page: No need to close the row

## Slide 18: 10K view on the latency
Page Empty: ACT + CAS
Page Hit: CAS
Page Miss: PRE+ACT+CAS

## Slide 19: DRAM Controller
LLC
Addr. Mapper
RQ WQ
DRAM
Controller
CQ
CQ
CQ
CQ
Command Scheduler
Data bus (burst length= eight beats each of 64-bits)
Command and Address bus
Frequency 800MHz
1066MHz
1333MHz
Frequency 1600MHz
2133MHz
2666MHz
Double Data Rate (DDR)

## Slide 20: Reads and Writes(Writebacks)
Reads are critical to performance
Write Queue stores writes and the writes are serviced after # writes reach a threshold
Why?
The direction of the data bus changes from reads to writes. So ??
DRAM controller creates DRAM commands from based on the requests at read Q and write Q

## Slide 21: DRAM Scheduling
FR-FCFS
Prefers requests with Row hits (column-first) FR: First Ready
Based on
Row-buffer locality, Source of the request, Loads/Stores
Load criticality
Satisfy all the timing constraints. Around 60

## Slide 22: DRAM Bandwidth
Names | Memory clock | I/O bus clock | Transfer rate | Theoretical bandwidth
DDR-200, PC-1600 | 100 MHz | 100 MHz | 200 MT/s | 1.6 GB/s
DDR-400, PC-3200 | 200 MHz | 200 MHz | 400 MT/s | 3.2 GB/s
DDR2-800, PC2-6400 | 200 MHz | 400 MHz | 800 MT/s | 6.4 GB/s
DDR3-1600, PC3-12800 | 200 MHz | 800 MHz | 1600 MT/s | 12.8 GB/s
DDR4-2400, PC4-19200 | 300 MHz | 1200 MHz | 2400 MT/s | 19.2 GB/s
DDR4-3200, PC4-25600 | 400 MHz | 1600 MHz | 3200 MT/s | 25.6 GB/s
DDR5-4800, PC5-38400 | 300 MHz | 2400 MHz | 4800 MT/s | 38.4 GB/s
DDR5-6400, PC5-51200 | 400 MHz | 3200 MHz | 6400 MT/s | 51.2 GB/s