## Slide 1: CS230: Digital Logic Design and Computer Architecture
Lecture 23: DRAM Controller and Cache Coherence
https://www.cse.iitb.ac.in/~biswa/courses/CS230/autumn23/main.html

## Slide 2: 10K view on the latency
Page Empty: ACT + CAS
Page Hit: CAS
Page Miss: PRE+ACT+CAS

## Slide 3: Rowhammer
Row of Cells
Row
Row
Row
Row
Wordline
VLOW
VHIGH
Victim Row
Victim Row
Aggressor Row
Repeatedly opening and closing a row induces disturbance errors in adjacent rows
Opened
Closed
Advanced Computer Architecture

## Slide 4: Rowhammer
Row of Cells
Row
Row
Row
Row
Wordline
VLOW
VHIGH
Victim Row
Victim Row
Aggressor Row
Opened
Closed
“It’s like breaking into an apartment by repeatedly slamming a neighbor’s door until the vibrations open the door you were after” – Motherboard Vice

## Slide 5: The Code Please
DDR3
DRAM Module
x86 CPU
X
111111111
111111111
111111111
111111111
111111111
111111111
Avoid cache hits
  Flush X from cache
Avoid row hits to X
  Read Y in another row
Y
Advanced Computer Architecture

## Slide 6: The code please
Y
X
111111111
111111111
111111111
111111111
111111111
111111111
loop:
mov (X), %eax
mov (Y), %ebx
clflush (X)
clflush (Y)
mfence
jmp loop
1111
1111
011011110
110001011
101111101
001110111

## Slide 7: Solution: DRAM Refresh
But intelligently 
Baseline: Once in 63ms
Need for a Rowhammer tracker, and then mitigator
Advanced Computer Architecture

## Slide 8: DRAM Controller
LLC
Addr. Mapper
RQ WQ
DRAM
Controller
CQ
CQ
CQ
CQ
Command Scheduler
Data bus (burst length= eight beats each of 64-bits)
Command and Address bus
Frequency 800MHz
1066MHz
1333MHz
Frequency 1600MHz
2133MHz
2666MHz
Double Data Rate (DDR)

## Slide 9: Reads and Writes(Writebacks)
Reads are critical to performance
Write Queue stores writes and the writes are serviced after # writes reach a threshold
Why?
The direction of the data bus changes from reads to writes. So ??
DRAM controller creates DRAM commands from based on the requests at read Q and write Q

## Slide 10: DRAM Scheduling
FR-FCFS
Prefers requests with Row hits (column-first) FR: First Ready
Based on
Row-buffer locality, Source of the request, Loads/Stores
Load criticality
Satisfy all the timing constraints. Around 60

## Slide 11: DRAM Bandwidth
Names | Memory clock | I/O bus clock | Transfer rate | Theoretical bandwidth
DDR-200, PC-1600 | 100 MHz | 100 MHz | 200 MT/s | 1.6 GB/s
DDR-400, PC-3200 | 200 MHz | 200 MHz | 400 MT/s | 3.2 GB/s
DDR2-800, PC2-6400 | 200 MHz | 400 MHz | 800 MT/s | 6.4 GB/s
DDR3-1600, PC3-12800 | 200 MHz | 800 MHz | 1600 MT/s | 12.8 GB/s
DDR4-2400, PC4-19200 | 300 MHz | 1200 MHz | 2400 MT/s | 19.2 GB/s
DDR4-3200, PC4-25600 | 400 MHz | 1600 MHz | 3200 MT/s | 25.6 GB/s
DDR5-4800, PC5-38400 | 300 MHz | 2400 MHz | 4800 MT/s | 38.4 GB/s
DDR5-6400, PC5-51200 | 400 MHz | 3200 MHz | 6400 MT/s | 51.2 GB/s

## Slide 12: Cache Coherence
P1
P3
P2
Cache
Bus
sum=0
LLC/DRAM

## Slide 13: Cache Coherence
P1
P3
P2
sum=0
sum =0
V
rd &sum
DRAM

## Slide 14: Cache Coherence
P1
P3
P2
sum=0
DRAM
sum=0
V
rd &sum
sum=0
V

## Slide 15: Cache Coherence
P1
P3
P2
sum=0
DRAM
sum=0
V
wr sum
(sum = 3)
3
D
sum=0
V

## Slide 16: Cache Coherence
P1
P3
P2
sum=0
DRAM
sum=3
D
sum=0
V
wr &sum
(sum = 7)
7
D

## Slide 17: The Problem
P1
P3
P2
sum=0
DRAM
sum=3
D
sum=7
D
rd &sum
print sum=3
Err!
Voila
print sum=7

## Slide 18: The Problem
If multiple cores cache the same block, how do they ensure they all see a consistent state?
Solution:
1. Write Propagation: All writes eventually become visible to other cores.
2. Write Serialization: All cores see write to a cache line in same order.
Need a protocol to ensure (1) and (2) called cache coherence protocol

## Slide 19: Invalidate/Update
  Invalidate –
  Write to a cache line, and simultaneously broadcast invalidation of address to all others
  Other cores clear/invalidate their cache lines
  Update –
  Write to a cache line, and simultaneously broadcast written data to all others
  Other cores update their caches if data was present

## Slide 20: A Simple MSI protocol
  Extend single valid bit per line to three states:
  M(odified): only one cache, memory not updated.
  S(hared): one or more caches, and memory copy is up-to-date
  I(nvalid): not present
Read - Read request on bus, transitions to S
Write - ReadEx request, transitions to M state

## Slide 21: State-transitions: Processor side (Master core)
M
I
S
PrRd/ –
PrWr/ –
PrWr/BusRdX
PrRd/BusRd
PrRd/ –
PrWr/BusRdX

## Slide 22: Bus-side (Rest of the cores)
M
I
S
BusRdX/Flush
BusRdX/ –
BusRd/ –
BusRd/Flush
BusRd/ –
BusRdX/ –

## Slide 23: MSI Protocol
P1
P3
P2
Cache
Bus
Snooper
Snooper
Snooper
X=1
DRAM

## Slide 24: MSI Protocol
P1
P3
P2
Snooper
Snooper
Snooper
X=1
DRAM
rd &X
BusRd

## Slide 25: MSI Protocol
P1
P3
P2
Snooper
Snooper
Snooper
X=1
DRAM
X=1
S

## Slide 26: MSI Protocol
P1
P3
P2
Snooper
Snooper
Snooper
X=1
DRAM
X=1
S
wr &X
(X=2)
M
2

## Slide 27: MSI Protocol
P1
P3
P2
Snooper
Snooper
Snooper
X=1
DRAM
X=2
M
rd &X
BusRd

## Slide 28: MSI Protocol
P1
P3
P2
Snooper
Snooper
Snooper
X=1
DRAM
X=2
M
X=2
S
2
S
Cancel DRAM read
Flush

## Slide 29: MSI Protocol
P1
P3
P2
Snooper
Snooper
Snooper
X=2
LLC
X=2
S
X=2
S
wr &X
X=3
BusRdX
I
M
3

## Slide 30: MSI Protocol
P1
P3
P2
Snooper
Snooper
Snooper
X=2
DRAM
X=2
I
X=3
M
rd &X
BusRd
S
3
Update DRAM as well
S
3
Flush

## Slide 31: MSI Protocol
P1
P3
P2
Snooper
Snooper
Snooper
X=3
DRAM
X=3
S
X=3
S
rd &X

## Slide 32: Summary: For your practice
Proc Action | State P1 | State P2 | State P3 | Bus Action | Data From
R1 | - | - | - | BusRd | Mem
W1 | - | - | - | BusRdX | Mem
R3 | - | - | - | BusRd | P1 cache
W3 | - | - | - | BusRdX | Mem
R1 | - | - | - | BusRd | P3 cache
R3 | - | - | - | - | -
R2 | - | - | - | BusRd | Mem

## Slide 33: Summary: For your practice
Proc Action | State P1 | State P2 | State P3 | Bus Action | Data From
R1 | S | - | - | BusRd | Mem
W1 | M | - | - | BusRdX | Mem
R3 | S | - | S | BusRd | P1 cache
W3 | I | - | M | BusRdX | Mem
R1 | S | - | S | BusRd | P3 cache
R3 | S | - | S | - | -
R2 | S | S | S | BusRd | Mem