## Slide 1: CS230: Digital Logic Design and Computer Architecture
Lecture 23: Connecting All the Dots (O3 processor)
https://www.cse.iitb.ac.in/~biswa/courses/CS230/autumn23/main.html

## Slide 2: Recap
Remember out-of-order processor
Inorder fetch, out-of-order execute, inorder commit
Now, we will discuss in details
Static scheduling: Compiler can do

## Slide 3: Tomasulo’s Organization for dynamic scheduling
FP adders
Add1
Add2
Add3
FP multipliers
Mult1
Mult2
From Mem
FP Registers
Reservation
Stations
To Mem
FP Op
Queue
Load Buffers
Store
Buffers
Load1
Load2
Load3
Load4
Load5
Load6

## Slide 4: Points to remember
Control & buffers distributed with Function Units (FU)
  FU buffers called “reservation stations”; have pending operands
Registers in instructions replaced by values or pointers to reservation stations(RS); called register renaming ;
  avoids WAR, WAW hazards
  More reservation stations than registers, so can do optimizations compilers can’t
Results to FU from RS over Common Data Bus that broadcasts results to all FUs
Load and Stores treated as FUs with RSs as wells
Decode stage of the pipeline: becomes two stages:
Issue: Decode instructions, check structural hazards
Read operands: Wait until no data hazards, then read operands.
Some processors use the term dispatch and issue.

## Slide 5: Reservation Station Components
Op: Operation to perform in the unit (e.g., + or –)
Vj, Vk: Value of Source operands
  Store buffers has V field, result to be stored
Qj, Qk: Reservation stations producing source registers (value to be written)
  Qj,Qk=0 => ready
  Store buffers only have Qi for RS producing result
Busy: Indicates reservation station or FU is busy
Register result status—Indicates which functional unit will write each register, if one exists. Blank when no pending instructions that will write that register.

## Slide 6: The New Pipeline
Inorder Instruction fetch
Fetched instructions enqueued into a Q called Instruction Q (IQ).
Inorder instruction issue from the IQ
Outoforder execution
New concept of register renaming through reservation stations that eliminates WAR and WAW hazards
Computer Architecture

## Slide 7: An Example
Think about memory hierarchy 
Computer Architecture

## Slide 8: Cycle 1
Load: 2 cycle
FP add: 2 cycles
FP multiply: 10 cycles
FP divide: 40 cycles
Computer Architecture

## Slide 9: Cycle 2
can have multiple loads outstanding
Computer Architecture

## Slide 10: Cycle 3: Continue doing it 
Note: registers names are removed (“renamed”) in Reservation Stations; MULT issued
Computer Architecture

## Slide 11: Register Renaming
Tomasulo provides Implicit Register Renaming
  User registers renamed to reservation station tags
Explicit Register Renaming:
  Use physical register file that is larger than number of registers specified by ISA
Keep a translation table:
  ISA register => physical register mapping
  Physical register becomes free when not being used by any instructions in progress. More later after ROB.

## Slide 12: Explicit Register Renaming
Rapid access to a table of translations
A physical register file that has more registers than specified by the ISA
Ability to figure out which physical registers are free.
  No free registers  stall on issue
Thus, register renaming doesn’t require reservation stations. However:
  Many modern architectures use explicit register renaming + Tomasulo-like reservation stations to control execution.

## Slide 13: Tomasulo, O3 completion, we need inorder complete (commit)
Instructions fetched and decoded into instruction
reorder buffer in-order
Execution is out-of-order (  out-of-order completion)
Commit (write-back to architectural state, i.e., regfile &
memory) is in-order
Temporary storage needed to hold results before commit (shadow registers and store buffers)
Fetch
Decode
Execute
Commit
Reorder Buffer
In-order
In-order
Out-of-order
Kill
Kill
Kill
Exception?
Inject handler PC

## Slide 14: Dynamic scheduling with speculative execution
Reorder
Buffer
FP
Op
Queue
FP Adder
FP Adder
Res Stations
Res Stations
FP Regs
Compar network
Need as many ports on ROB as register file
Reorder Table
Dest Reg
Result
Exceptions?
Valid
Program Counter

## Slide 15: Speculative O3 with Tomasulo and ROB
1. Issue—get instruction from FP Op Queue
  If reservation station and reorder buffer slot free, issue instr & send operands & reorder buffer no. for destination (this stage sometimes called “dispatch”)
2. Execution—operate on operands (EX)
  When both operands ready then execute; if not ready, watch CDB for result; when both in reservation station, execute; checks RAW (sometimes called “issue”)
3. Write result—finish execution (WB)
  Write on Common Data Bus to all awaiting FUs & reorder buffer; mark reservation station available.
4. Commit—When instruction reaches head of the ROB, update register with reorder result
  When instr. at head of reorder buffer & result present, update register with result (or store to memory) and remove instr from reorder buffer. Mispredicted branch flushes reorder buffer (sometimes called “graduation”)

## Slide 16
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F0
LD F0,10(R2)
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
1 10+R2
Dest
Reorder Buffer
Registers

## Slide 17
2 ADDD R(F4),ROB1
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F10
F0
ADDD F10,F4,F0
LD F0,10(R2)
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
1 10+R2
Dest
Reorder Buffer
Registers

## Slide 18
3 DIVD ROB2,R(F6)
2 ADDD R(F4),ROB1
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F2
F10
F0
DIVD F2,F10,F6
ADDD F10,F4,F0
LD F0,10(R2)
N
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
1 10+R2
Dest
Reorder Buffer
Registers
If the predicted taken path is wrong,
flush out all instructions from the ROB
and reissue in the correct order
Remember exception/page
fault handling gets resolved
when the instruction
reaches the head of the ROB

## Slide 19: Memory Disambiguation
Question: Given a load that follows a store in program order, are the two related?
  (Alternatively: is there a RAW hazard between the store and the load)? Eg: st 0(R2),R5 ld R6,0(R3)
Can we go ahead and start the load early?
  Answer is that we are not allowed to start load until we know that address 0(R2)  0(R3)

## Slide 20: PAUSE: The out-of-order Madness
Compiler order
Processor order
Cache hierarchy order: MSHR
DRAM order: Remember FR-FCFS

## Slide 21: Summary of CS230 
Out-of-order course
teaching
how to ………….

## Slide 22: After this lecture
If you say branch resolution takes two/three cycles then 
On Friday, we will connect all the dots on the chalk-board